## Slide 1
QM30VT3
QM30VT3 3-Axis Vibration Sensor

## Slide 3: 3-Axis Vibration Sensors
3 axes of calculated overall scalar data
  Ultra Low Noise 3rd axis has improved accuracy over competitive tri-axial sensors
  New overall metrics added for additional flexibility in data monitoring
Onboard Vibe-IQ auto thresholding
  No longer required to have a Script running on our gateways to get the benefit of Machine Learning
NEW! High Frequency Enveloping (HFE)
  Standard sensor can monitor assets that we previously were not able to
NEW! Adjustable Fmax and Sample Length
  Users have expanded capabilities to configure the sensor
QM30VT3-MQP
List Price $320 USD
QM30VT3-SS-MQP
List Price $457 USD

## Slide 4
Onboard Vibe-IQ
Vibe-IQ is a Machine Learning Algorithm developed by Banner Engineering to simplify setting alerts
Baselines equipment by monitoring RMS Velocity and High-Frequency RMS Acceleration digital overall metrics in all 3 axes
Sets Warning and Alarm thresholds for each of the baseline values automatically based how the equipment is running now
Run Flag disregards any samples that are taken when the machine is not operational
Baseline time and sample frequency are adjustable to ensure an accurate snapshot of what normal operation is for every asset

## Slide 5: Vibration – What do these values tell you?
  RMS Velocity [10 – 1000 Hz]
    Indicates issues such as: soft foot, misalignment, unbalance, etc.
  High Frequency RMS Acceleration [1000 – 4000 Hz]
    Indicates early bearing failure

## Slide 6
High Frequency Enveloping (HFE)
Adjust Sample Frequency and Fmax
Advanced users can be more precise on evaluating FFT data by manipulating the bin size and separating frequency spikes
Sample time can be shortened for applications that need rapid response for lower frequency faults
Pinch and zoom flexibility to allow advanced users to focus on specific fault indicators
Uses demodulation to match common views from vibration analyzers by emphasizing lower amplitude repeating signals
Improves our ability to detect early bearing related faults on slower moving equipment
HFE affects how we generate the vibration signal, our High-Frequency vibration overalls are calculated with information that has used this filtering method

## Slide 7: Vibration Mounting Accessories
QM30VT3-MQP 150mm cable with M12, Aluminum
QM30VT3-SS-MQP 150mm cable with M12, Stainless
BWA-QM30-CMAL
Magnet Mount, Curved Surface, Aluminum
BWA-QM30-FMSS
Magnet Mount, Flat Surface, Stainless
BWA-QM30-CEAL
Epoxy Mount, Curved Surface, Aluminum, pack of 5
Rapid Release, Flat Surface, Aluminum
BWA-QM30-FSALR
BWA-QM30-FSSSR
Rapid Release, Flat Surface, Stainless
BWA-QM30-FTAL
Stud/Tape Mount, Flat Surface, Aluminum
BWA-QM30-FTSS
Stud/Tape Mount, Flat Surface, Stainless

## Slide 8: Sensor Mounting Methods

## Slide 9: QM30VT3 Compatibility with AMG
Update to .DAT required
  Defines which devices and registers are used by the AMG
  File and instructions for updating will be found on AMG series page
Compatible with Banner CDS
AMG Update (coming soon)
  Fixed a scaling issue with the Power Usage feature for CT and Rogowski Coils
  Historic View of data (Graph)

## Slide 10: Why Monitor Vibration?
Early Fault Detection
Prevent Catastrophic Failures
Provide time for acquiring parts, or alternate equipment
Prevent unscheduled downtime
Condition
Time
Preventive
Maintenance
Predictive
Maintenance
Operator
Care
Run to Failure
Vibration analysis
Low risk
Alarm
High risk
Oil analysis
Temperature rise
Audible noise
Too hot to touch
Mechanically loose
Catastrophic
Failure

## Slide 11
Wireless 3-Axis Solutions

## Slide 12: Wireless 3 axis solutions
QM30VT3-MQP
List Price $320 USD
QM30VT3-SS-MQP
List Price $457 USD
DX80DR9MQ45VA3C
List Price $399 USD
3 Axis MH solutions for battery powered systems
DX80DR9MQ45VT3-5QD NB
(MH Battery)
R70SR9MQ
(Line Powered
Serial or MH Radio)
List Price $214 USD
List Price $349 USD

## Slide 13
Wireless 2-Axis Solutions

## Slide 14: Wireless 2 axis solutions
QM30VT1
List Price $279 USD
QM30VT1-SS
List Price $480 USD
DX80N9Q45VTP
List Price $321 USD
DX80N9Q45VTPD
List Price $374 USD
2 Axis Performance solutions live on
DX80N9Q45VAC
List Price $348 USD

## Slide 15: QM30VT3: Launch Sales Resources
QM30VT3
Sell Sheet
Videos
  QM30VT3 Vibration Basics
  How to Install/Best Practices
  How to use Vibe-IQ
Part Pages:
  QM30VT3 Modbus
  Q45VA3C All-in-One
  Q45VT3 Radio
Application Images
Data Sheets